## Slide 1: Coordinate Systems, Datums and Map Projections D’Arcangelis 11/9/09

## Slide 2
Every map user and maker should have a basic understanding of projections, no matter how much computers seem to have automated the process.
Hmmm…

## Slide 3: Why is this important?
Creating spatial data (collecting GPS data)
Import into GIS and overlay with other layers
Acquiring spatial data from other sources
Display your GPS data using maps

## Slide 4: Coordinate Systems
There are 2 types of coordinate systems:
  Geographic Coordinate Systems
  Projected Coordinate Systems

## Slide 5: Geographic Coordinate System
A reference system using latitude and longitude to define the location of points on the surface of a sphere or spheroid
  decimal degrees (DD) -92.5
  degrees/minutes/seconds (DMS) 92° 30’ 00” W

## Slide 6: Geographic Coordinate System
- Earth is not a sphere
- Poles are flattened
- Bulges at equator
Earth is a spheroid……or ellipsoid
Notes: USE GLOBE for PROP!
In order to transform Lat/Lon into these various projections. A model of the shape of the earth has to be developed so these computations can be performed.
A model to describe the shape of the earth is called the ellipsoid/spheroid.

## Slide 7: Geographic Coordinate System
Spheroid approximates the shape of the earth
  Model of the earth
  Essentially when surveyors get together and all agree to be wrong
  Also called an “ellipsoid”

## Slide 8: Geographic Coordinate System
A datum defines the position of the spheroid relative to the center of the earth
  Origin and orientation of latitude and longitude lines are determined by the datum
  Hundreds of datums customized for different parts of the world

## Slide 9: Common Datums used in U.S.
North American Datum 1927 (NAD27)
  Uses the Clarke 1866 spheroid
  Reference point is located at Meades Ranch, Kansas
  Based on ground survey inrmation in the 1800’s
North American Datum 1983 (NAD83)
  Uses GRS80 (Geodetic Reference System) spheroid
  Ellipsoid model from geocentric perspective
  Based on ground surveys and satellite information
WGS 1984
  Most recently developed datum/ framework for measurements worldwide
  Earth centered, or geocentric, perspective
  This is the datum used by all GPS satellites
  Nearly identical to NAD83…therefore NAD83 is compatible with data collected in GPS using WGS84!
Notes: Ask if anyone knows what the ellipsoid represents? SHAPE OF THE EARTH
Is the spheroid and ellipsoid the same? YES

## Slide 10: Transforming between datums
Several methods available for transforming between NAD27 and NAD83
Standard and most accurate is NADCON
  Available in ArcView 8.x (ArcToolbox)
Many GPS devices transform using less accurate transformations
If you your GIS data is in NAD27, you should considering collecting in NAD83/WGS84 and transform your coordinates using ArcToolbox
  See “Appendix A” in TEC7132 course book on how to perform datum transformation using ArcToolbox

## Slide 11: Geographic Coordinate System
Universal Coordinate System (lat/long)
Lat/long is good for locating positions on surface of a globe
Lat/long is not efficient for measuring distances and areas!
  Latitude and longitude are not uniform units of measure
  One degree of longitude at equator = 111.321 km (Clarke 1866 spheroid)
  One degree of longitude at 60° latitude = 55.802 km (Clarke 1866 spheroid)

## Slide 12: Projected Coordinate Systems
A map projection is the systematic transformation of locations on the earth (latitude/longitude) to planar coordinates
The basis for this transformation is the geographic coordinate system (which references a datum)
Map projections are designed for specific purposes

## Slide 13: This process of flattening the earth will cause distortions in one or more of the following spatial properties:
Shape
  Conformal map projections preserve shape
Area
  Equal area map projections preserve area
Distance/Scale
  Equidistant map projections preserve distance
Direction/Angle
  Azimuthal map projections preserve true direction
Notes: All maps have errors. Something has to be sacrificed when choosing a projection.
These are the major characteristics which can be affected.
Maps that preserve Area are called Equal Area projections.
What type of map projection do you think would be used on maps used by sailors? Azimuthal/Equidistant

## Slide 14: Sinusoidal Projection
Notes: Ask class what type of map characteristic is preserved in this projection.
EQUAL AREA - areas on map proportional to areas on earth.
Used frequently in Atlases to show sedimentary basins throughout the world.

## Slide 15: Mercator Projection
Notes: Ask class what characteristic is preserved in this projection. SHAPE
CONFORMAL
Distortion increases away from Equator and extreme in polar regions.
Conformal - angles and shapes preserved within any small area are preserved.

## Slide 16: Universal Transverse Mercator (UTM)
Developed by military
Grid system
Earth divided into 60 zones
Great for small areas
  minimal map distortion
  distortion greater at edge of zones
Most common map projection used by NWRs
Notes: Handouts which talk about UTM will be handed out.

## Slide 17
Zone 1
International Date
Line - 180
Equator
Zone 18
o
Universal Transverse Mercator- Grid

## Slide 18: State Plane Coordinate System
To support high-accuracy applications, all US states have adopted their own specialized coordinate systems: State Plane Coordinates. For example, Texas has five zones based on the Lambert Conformal Conic projection, while Hawaii has five zones based on Transverse Mercator projection.
http://www.pipeline.com/~rking/spc.htm

## Slide 20: When GPS points don’t align with GIS Data
There are huge errors…data points do not overlay
Features could be displayed in wrong state or hemisphere!
Most likely a projection issue if:
Notes: Go into ArcView and demonstrate:
-decimal degrees Fedlands with UTM Zone 15 map of Minnesota
they do not overlay
view to full extent
-habitat map for bird survey in NAD83 with MR. Sid image which is in NAD27 (upper Mississippi example)
overlay in View - but not accurately align
SCALE Issue? Datum issue?
In this case it is a datum issue

## Slide 21: When GPS points don’t align with GIS Data
GPS data overlays with GIS data, but off by several hundred feet
Differences between NAD27 and NAD83 can be as much as 500 feet
This creates problems when doing analysis
Possibly a datum issue if:
Notes: Go into ArcView and demonstrate:
-decimal degrees Fedlands with UTM Zone 15 map of Minnesota
they do not overlay
view to full extent
-habitat map for bird survey in NAD83 with MR. Sid image which is in NAD27 (upper Mississippi example)
overlay in View - but not accurately align
SCALE Issue? Datum issue?
In this case it is a datum issue

## Slide 22: Conclusion
All maps are centered on a point or plane
Different projections cause maps to display spatial data differently
Careful thought toward map projection must be made in order to display data correctly